## Slide 1: Landscape Change Monitoring System (LCMS)
Project Overview
Data Applications
Data Access

## Slide 2: Agenda
10am: 1. Landscape Change Monitoring System (LCMS) Introduction
  1.1 Continental-scale geospatial computing in the Forest Service
  1.2 Overview of LCMS
  1.3 LCMS Workflow
  1.4 LCMS Applications
11am: Break
11:15am: 2. LCMS Data Access
2.1 LCMS Data Explorer Demo
2.2 LCMS in ArcPro
2.3 LCMS in Google Earth Engine
LCMS Homepage

## Slide 3: Learning objectives
Learn about the LCMS change, land cover and land use data products. Be able to describe the classes in each layer, and the date range and areas for which they are available.
Learn how LCMS products are generated. Gain an introduction to time series change detection, LandTrendr, CCDC, training data collection, random forest modeling, and map assemblage.
Learn how to access LCMS data products via the LCMS Data Explorer and the Google Earth Engine Data Catalog

## Slide 4: 1.1: Continental-Scale Geospatial Computing in the Forest Service

## Slide 5: The goal: understand how our landscape has changed in the past, and monitor how it continues to change.
1.1
Notes: If you’ve worked with GEE at all, you’re familiar with the data catalog. You’ve heard about the petabytes of data that are stored there. And it’s impressive! There are decades worth of imagery data, supporting terrestrial and aquatic datasets, land cover, elevation, etc. And all we have to do is figure out how to use it. You’re watching this training, you know what it’s about.
The US Forest Service has the same objectives as many of you all– use these data to understand patterns in how our landscape has changed in the past, and monitor how it continues to change in the future.

## Slide 6: The tool: Google Earth Engine (GEE)
Image: Google Earth Engine Data Catalog
Notes: - A cloud-based geospatial processing platform for executing large-scale environmental data analysis.
- Remote sensing and geospatial data archive:
  Petabytes of data in one location

## Slide 7: GEE’s freely-available satellite imagery and cloud computation make LCMS possible. Thousands of images are available, dating back to 1984.
Video: USGS + NASA
Notes: The reason why this is possible is that earth observing satellites have been circling the globe since the 1960s and routinely doing so since 1984 using a satellite system called Landsat.
In this animation you see how Landsat collects a narrow ribbon of imagery over the globe every day, skipping forward a little each day to cover the entire globe.
Every 16 days Landsat completes this worldwide image and starts over again.
Unfortunately until recently, being able to unlock the information in all of these images has been technically and economically impossible.
Only in the past decade we have been able to reveal some of the information contained in those images.
And the computation capabilities of GEE mean that we can chug through all of those data

## Slide 8: Continental-scale computation Example USFS Use Cases
FS needs to process a lot of data for many different applications:
Near real-time monitoring
Long term / multi-decadal trend monitoring
Snapshot-in-time: vegetation mapping
GUIs for data exploration
Notes: Long term / decadal trend monitoring is where we’re focusing today

## Slide 9: Continental-scale computation Example USFS Use Cases
FS needs to process a lot of data for many different applications:
Near real-time monitoring
Long term / multi-decadal trend monitoring
Snapshot-in-time: vegetation mapping
GUIs for data exploration
Notes: Long term / decadal trend monitoring is where we’re focusing today

## Slide 10: GTAC Use Case
Near-real time monitoring
  Burned Area Emergency Response (BAER)
  DeltaViewer Change Detection Method
  Landscape Automated Monitoring and Detection Algorithm (LAMDA)
Long term / decadal monitoring
  Monitoring Trends in Burn Severity (MTBS)
  Tree Canopy Cover (TCC)
  LCMS
Snapshot-in-time
  Vegetation mapping – 30+ classes
GUIs for data exploration
  MTBS
  TreeMap
  LCMS
Image: MTBS. Fire scar viewed in SWIR composite, Beaver Fire, California, USA, 2014
Notes: Describe each bolded title - refer to links as examples of what we’ve done.
In the USFS use case, Earth engine:
Vastly powerful applications
Can go over large spatial and temporal scales
Relies on the EE API for part or all of the workflow
Often needs other specialized tools or libraries

## Slide 11: GTAC Use Case
Landscape Change Monitoring System (LCMS)
Annual data layers of:
Vegetation cover Change
Land Cover
Land Use
Graphic: Change in size of the Columbia Glacier, Alaska
Notes: For this workshop, we’ll specifically be talking about LCMS. – which is just one example of how the USFS uses EE.
LCMS produces annual layers of vegetation cover change, land cover, and land use for the contiguous united states, alaska, puerto rico, and the us virgin islands

## Slide 12: 1.2: Overview of LCMS

## Slide 13: LCMS: The Story of a Place
Ensemble-based change detection system
Landsat TM & OLI and Sentinel-2 time series data record (1984-2022)
Pixel-based maps of Vegetation Loss, Gain, Land Cover, & Land Use
Landscape Change Monitoring System
1999
2001
2007
2011
Notes: DUPE FOR ACCESSIBLE IMAGE
LCMS is an ensemble-based change detection system that leverages the Landsat and Sentinel-2 data record to produce pixel-based maps of vegetative loss & gain as well as land cover and land use for every year since 1985.
We can think of this as the story of a place.

## Slide 14: LCMS: The Story of a Place
Ensemble-based change detection system
Landsat TM & OLI and Sentinel-2 time series data record (1984-2022)
Pixel-based maps of Vegetation Loss, Gain, Land Cover, & Land Use
Landscape Change Monitoring System
Notes: LCMS is an ensemble-based change detection system that leverages the Landsat and Sentinel-2 data record to produce pixel-based maps of vegetative loss & gain as well as land cover and land use for every year since 1985.
We can think of this as the story of a place.

## Slide 15: Current data coverage
Southeastern Alaska
Conterminous US
Puerto Rico and US Virgin Islands
1985-2022, updated annually
Notes: DUPE FOR ACCESSIBLE IMAGES
Hawaii is forthcoming

## Slide 16: Current data coverage
1985-2022, updated annually
Notes: Hawaii is forthcoming

## Slide 17: Planned data coverage
Change, land cover, and land use for Hawaii (ETA fall 2024)
Change, land cover, and land use for interior Alaska (ETA fall 2025)
Change attribution
  Classes: Harvest, fire, insect/disease/climate stress, storm event, water desiccation, water inundation, drought, southern pine beetle, loss in non-treed landscapes
Southeastern Alaska
Notes: Hawaii is forthcoming

## Slide 18: LCMS Products - Change
For each year: 1985-2022
For each 30m x 30m pixel
1985-2022
30m spatial resolution

## Slide 19: LCMS Products
Change: Fast Loss, Slow Loss, and Gain
Vegetation change largely caused by timber harvest and wildfire in the Willamette National Forest, Oregon, USA.
Slow Loss
Fast Loss
Gain
Change

## Slide 20: LCMS Products
Change: Fast Loss, Slow Loss, and Gain
Changes from insects, disease, and wildfire, Colorado, USA.
Slow Loss
Fast Loss
Gain
Change

## Slide 21: LCMS Products
Land Cover
Decrease in size of Great Salt Lake, Utah, USA.

## Slide 22: LCMS Products
Land Use
Urban expansion in Las Vegas, Nevada, USA.

## Slide 23: LCMS Products
Data access
LCMS products for CONUS, Southeastern Alaska, Puerto Rico, and the US Virgin Islands are available in the GEE Data Catalog.
Notes: LCMS publishes each of its releases in the GEE Data Catalog
Each year, an entire new time series of outputs is released from 1985 to the most recent completed growing season
This allows for methods to change, while ensuring data continuity for each new year’s release back to 1985.

## Slide 24: Satellite Data Record
Landsat
Sentinel-2
30m
30m
30m
30m
Notes: DUPE FOR ACCESSIBLE IMAGES
Landsat:
1984-Present
~7-14 days
30m x 30m spatial resolution
Includes Landsat satellites 4-9
Sentinel-2
2016-present
~5 days
10m x 10m resolution for many bands; 20m x 20m spatial resolution for SWIR
Sentinel-2 data are resampled to 30m resolution for LCMS

## Slide 25: Satellite Data Record
Landsat
Sentinel-2
Notes: Landsat:
1984-Present
~7-14 days
30m x 30m spatial resolution
Includes Landsat satellites 4-9
Sentinel-2
2016-present
~5 days
10m x 10m resolution for many bands; 20m x 20m spatial resolution for SWIR
Sentinel-2 data are resampled to 30m resolution for LCMS

## Slide 26: Satellite Data Record
Landsat
1984-Present
~7-14 days
30m x 30m spatial resolution
Includes Landsat satellites 4-9
Sentinel-2
2016-present
~5 days
10m x 10m and 20m x 20m spatial resolution
Sentinel-2 data are resampled to 30m resolution
Figure from USGS
Notes: Landsat and Sentinel-2 have many similarities and differences
The graphic shows how each band compares between the different sensors/platforms
After sentinel-2 came online in 2016, we got access to data with much higher temporal resolution - collected more frequently– and spatial resolution– 10 or 20m, compared to 30m with Landsat.

## Slide 27: 1.3: LCMS Workflow

## Slide 28: LCMS Workflow
OUTPUT
POST-
PROCESSING
PROCESS
BASE-
LEARNERS
INPUT
Terrain variables
LCMS raster outputs
annual
Landsat + Sentinel-2 composites
LandTrendr
CCDC
all
Landsat
map assemblage
map validation
set colors, no data values, etc
Training data -
TimeSync
statistical models
Notes: DUPE FOR ACCESSIBLE IMAGES
Robust stack of predictor data and robust training data are the foundation of the LCMS product.
Spectral data from earth observing satellites – Landsat and Sentinel-2
LCMS uses TimeSync data for training data. TimeSync is a manual image interpretation tool where interpreters use spectral reflectance data, satellite and aircraft imagery, and other existing datasets to determine the appropriate classifications at 30m x 30m plots across the our study areas. The training point locations are determined using a stratified random sampling approach. There are about 10,000 training TimeSync plots for the CONUS and around 1000 for southeastern Alaska and Puerto Rico US Virgin islands each
Here are the numbers of the lab and lecture sections where we’ll discuss each of these parts!

## Slide 29: LCMS Workflow
Notes: Robust stack of predictor data and robust training data are the foundation of the LCMS product.
Spectral data from earth observing satellites – Landsat and Sentinel-2
LCMS uses TimeSync data for training data. TimeSync is a manual image interpretation tool where interpreters use spectral reflectance data, satellite and aircraft imagery, and other existing datasets to determine the appropriate classifications at 30m x 30m plots across the our study areas. The training point locations are determined using a stratified random sampling approach. There are about 10,000 training TimeSync plots for the CONUS and around 1000 for southeastern Alaska and Puerto Rico US Virgin islands each
Here are the numbers of the lab and lecture sections where we’ll discuss each of these parts!

## Slide 30: LCMS Workflow Landsat and Sentinel-2 composites
Mask clouds and cloud shadows
Take the medoid of the values to create an annual composite
  Landsat 4 TM
  Landsat 5 TM
  Landsat 7 ETM+
  Landsat 8 OLI
  Landsat 9 OLI-2
  Sentinel-2
annual
Landsat + Sentinel-2 composites
Notes: Gather all available Landsat 4-9 and Sentinel 2a and 2b for each year for each study area
Find common bands and give descriptive band names (e.g. blue, green, red, nir, swir1, swir2)
Mask clouds and cloud shadows using a variety of methods that are available
Take the medoid value for each band from the remaining values– closest real pixel value to the median.
We get one composite for each year.

## Slide 31: LCMS Workflow Landsat and Sentinel-2 composites
Figure from the LT-GEE Guide
Mask clouds and cloud shadows
Take the medoid of the values to create an annual composite
  Landsat 4 TM
  Landsat 5 TM
  Landsat 7 ETM+
  Landsat 8 OLI
  Landsat 9 OLI-2
  Sentinel-2
annual
Landsat + Sentinel-2 composites
Notes: If you look at how spectral indices from one pixel change throughout the 35 years of composites, you can get an idea for what has happened on the landscape.

## Slide 32: LCMS Workflow LandTrendr
Fit linear segments to a time series of annual composites
Segments describe periods of the same change process, land cover, and/or land use type
Gain additional information from length of segment, steepness of slope, and position of vertex
Figure from the LT-GEE Guide
Loss
Stable
Gain
LandTrendr
Notes: DUPE FOR ACCESSIBLE IMAGES
Our raw composite values still have some inter-annual variability that we would not want to call “Change”
LandTrendr helps us fit lines through periods of similar change, land cover, and/or land use to reduce noise
Here is that pixel’s spectral values in graph form. The change algorithms LandTrendr basically fit segments to the raw composite values from the satellite (lower figure), that can then be interpreted as segments of “Stable”, “Loss”, or “Gain.”

## Slide 33: LCMS Workflow LandTrendr
Fit linear segments to a time series of annual composites
Segments describe periods of the same change process, land cover, and/or land use type
Gain additional information from length of segment, steepness of slope, and position of vertex
Figures adapted from the LT-GEE Guide
LandTrendr
Notes: Our raw composite values still have some inter-annual variability that we would not want to call “Change”
LandTrendr helps us fit lines through periods of similar change, land cover, and/or land use to reduce noise
Here is that pixel’s spectral values in graph form. The change algorithms LandTrendr basically fit segments to the raw composite values from the satellite (lower figure), that can then be interpreted as segments of “Stable”, “Loss”, or “Gain.”

## Slide 34: LCMS Workflow Continuous Change Detection and Classification (CCDC)
CCDC
Figure: Arévalo et al. 2020, Figure 2,
Notes: CCDC is another method for breaking the time series into similar segments
CCDC looks for periods of time with similar seasonality (phenology)
Here is a pixel’s spectral values in graph form.
CCDC fits a harmonic curve to the raw values from the satellite (lower figure). If values change significantly from the current harmonic curve, a new harmonic model will be fit.
Continuous Change Detection and Classification
Utilizes every available cloud and cloud shadow-free observation to provide information on intra-annual change and seasonality
A departure from the seasonality signature indicates a change
We use the predicted value based on the harmonic model, the model’s coefficients, and the difference between the current year and the previous year’s fitted values as the slope to allow CCDC to work properly within the LCMS annual ensemble framework.

## Slide 35: LCMS Workflow Temporal segmentation
We use multiple algorithms because combining them gives us lower error.
Objective: balance omission error and comission error
Healey et al. 2018
Healey et al. 2018 - Figure 3
CCDC
LandTrendr
Notes: Healey et al 2018 showed all change detection algorithms have a high error rate on their own relative to TimeSync-based reference data
If you take these individual algorithms and use them in a supervised classification model, you can lower error rates
But error rates still remain high compared to TimeSync reference data

## Slide 36: LCMS Workflow Training Data
TimeSync
Stratified random sampling across change, land cover, and land use types
~10,000 training TimeSync plots for CONUS
~ 1,000 each for southeastern Alaska and Puerto Rico-US Virgin Islands
30m
30m
Training data -
TimeSync
Notes: DUPE FOR ACCESSIBLE IMAGES
LCMS uses TimeSync data for training data. TimeSync is a manual image interpretation tool where interpreters use spectral reflectance data, satellite and aircraft imagery, and other existing datasets to determine the appropriate classifications at 30m x 30m plots across the our study areas. The training point locations are determined using a stratified random sampling approach. There are about 10,000 training TimeSync plots for the CONUS and around 1000 for southeastern Alaska and Puerto Rico US Virgin islands each
Each plot is manually interpreted for change process (e.g. harvest, fire, growth, etc..), land cover (e.g. trees, grass, water, etc…), and land use (e.g. developed, forest, rangeland, etc…) for each year

## Slide 37: LCMS Workflow Training Data
TimeSync
Stratified random sampling across change, land cover, and land use types
~10,000 training TimeSync plots for CONUS
~ 1,000 each for southeastern Alaska and Puerto Rico-US Virgin Islands
Training data -
TimeSync
Notes: LCMS uses TimeSync data for training data. TimeSync is a manual image interpretation tool where interpreters use spectral reflectance data, satellite and aircraft imagery, and other existing datasets to determine the appropriate classifications at 30m x 30m plots across the our study areas. The training point locations are determined using a stratified random sampling approach. There are about 10,000 training TimeSync plots for the CONUS and around 1000 for southeastern Alaska and Puerto Rico US Virgin islands each
Each plot is manually interpreted for change process (e.g. harvest, fire, growth, etc..), land cover (e.g. trees, grass, water, etc…), and land use (e.g. developed, forest, rangeland, etc…) for each year

## Slide 38: LCMS Workflow Training Data - Manual Interpretation
Training data -
TimeSync
TimeSync
Manually interpreted time series classify change type, land use, and land cover for each year at each plot
Stable
Stable
Loss
Gain
Notes: DUPE FOR ACCESSIBLE IMAGES
LCMS uses TimeSync data for training data. TimeSync is a manual image interpretation tool where interpreters use spectral reflectance data, satellite and aircraft imagery, and other existing datasets to determine the appropriate classifications at 30m x 30m plots across the our study areas. The training point locations are determined using a stratified random sampling approach. There are about 10,000 training TimeSync plots for the CONUS and around 1000 for southeastern Alaska and Puerto Rico US Virgin islands each
Each plot is manually interpreted for change process (e.g. harvest, fire, growth, etc..), land cover (e.g. trees, grass, water, etc…), and land use (e.g. developed, forest, rangeland, etc…) for each year

## Slide 39: LCMS Workflow Training Data - Manual Interpretation
Training data -
TimeSync
TimeSync
Manually interpreted time series classify change type, land use, and land cover for each year at each plot
Notes: LCMS uses TimeSync data for training data. TimeSync is a manual image interpretation tool where interpreters use spectral reflectance data, satellite and aircraft imagery, and other existing datasets to determine the appropriate classifications at 30m x 30m plots across the our study areas. The training point locations are determined using a stratified random sampling approach. There are about 10,000 training TimeSync plots for the CONUS and around 1000 for southeastern Alaska and Puerto Rico US Virgin islands each
Each plot is manually interpreted for change process (e.g. harvest, fire, growth, etc..), land cover (e.g. trees, grass, water, etc…), and land use (e.g. developed, forest, rangeland, etc…) for each year

## Slide 40: LCMS Workflow Training Data - Manual Interpretation
Change Process | Land Cover | Land Use (primary and secondary)
Stable Harvest Mechanical Fire Hydrology/flooding Wind Spectral decline Structural decline Growth/recovery | Tree Tall Shrubs Shrub Grass/Forb/Herb Impervious Barren Snow/Ice Water | Forest Developed Agriculture Non-forest Wetland Rangeland/Pasture Other
Notes: Classes included in our various products (*Land cover there are some mixed classes not shown here such as Tree-Shrub)
In Timesync our interpreters assigned a Change Process, Land Cover, and Land Use class to each year of the plot’s history. This information is then used to train RF models (This is covered in Modules 4 and 5)
Note, Tall Shrubs and Snow/Ice classes are included as a dummy variables in PRUSVI, as there are no Tall Shrubs or Snow/Ice modeled for the land cover maps

## Slide 41: LCMS Workflow Training Data - Manual Interpretation
Change Type | Change Process | Land Cover | Land Use (primary and secondary)
Stable Loss Gain | Stable Harvest Mechanical Fire Hydrology/flooding Wind Spectral decline Structural decline Growth/recovery | Tree Tall Shrubs Shrub Grass/Forb/Herb Impervious Barren Snow/Ice Water | Forest Developed Agriculture Non-forest Wetland Rangeland/Pasture Other
Change Process | Land Cover | Land Use (primary and secondary)
Stable Harvest Mechanical Fire Hydrology/flooding Wind Spectral decline Structural decline Growth/recovery | Tree Tall Shrubs Shrub Grass/Forb/Herb Impervious Barren Snow/Ice Water | Forest Developed Agriculture Non-forest Wetland Rangeland/Pasture Other
Notes: Currently, we group the Change Process call into stable, loss, and gain.
Classes included in our various products (*Land cover there are some mixed classes not shown here such as Tree-Shrub)
In Timesync our interpreters assigned a Change call, a Land Use class, and a Land Cover class to each year of the plot’s history. This information was used then used when building our RF models (This is covered in Modules 4 and 5)
Note, Tall Shrubs and Snow/Ice classes are included as a dummy variables in PRUSVI, as there are no Tall Shrubs or Snow/Ice modeled for the land cover maps

## Slide 42: LCMS Workflow Terrain variables
Calculated from DEM
  USGS 3DEP 10m
Variables include:
  Elevation
  Slope
  Aspect
  Topographic Position Indices
Terrain variables
Notes: Terrain variables are a great proxy for climate information
These include elevation, slope, aspect, and topographic position indices

## Slide 43: LCMS Workflow Statistical models
Random Forest model
“Ensemble model” because of the suite of predictor variables
Composed of many Classification and Regression Tree (CART) models
Output: probability that a pixel belongs to a certain class
No Loss
Loss
statistical models
Notes: Use TimeSync training data to build RF models and apply them on a pixel-wise basis
Example here there are two possible outcomes (leaf nodes) for a given decision tree – loss or no loss.
For a given LCMS class we determine the optimal number of decision trees and maximum number of predictors to consider (model tuning) to generate a RF model (ensemble of CART models)
Use ee.Classifier.smileRandomForest algorithm in GEE

## Slide 44: LCMS Workflow Statistical models
Random Forest model
“Ensemble model” because of the suite of predictor variables
Composed of many Classification and Regression Tree (CART) models
Output: probability that a pixel belongs to a certain class
statistical models
Notes: Use TimeSync training data to build RF models and apply them on a pixel-wise basis
Example here there are two possible outcomes (leaf nodes) for a given decision tree – loss or no loss.
For a given LCMS class we determine the optimal number of decision trees and maximum number of predictors to consider (model tuning) to generate a RF model (ensemble of CART models)
Use ee.Classifier.smileRandomForest algorithm in GEE

## Slide 45: LCMS Workflow Statistical models
Crop
Grass
Grass
Shrub
Grass
Class | Prob. | Final class
Grass | 60% | GRASS
Shrub | 20% | 
Crop | 20% | 
Random Forest model
“Ensemble model” because of the suite of predictor variables
Composed of many Classification and Regression Tree (CART) models
Output: probability that a pixel belongs to a certain class
statistical models
Notes: DUPE FOR ACCESSIBLE IMAGES
Apply RF model for a given class on pixel-wise basis to generate model outputs
E.g. 4 out of 5 trees predicted grass (60% probability)
We use thresholding for the change product ( thresholding is based on accuracy assessment using predicted and validation data) to determine if change occurred or not.
If we take the class with the majority of the votes, this pixel would be grass

## Slide 46: LCMS Workflow Statistical models
Random Forest model
“Ensemble model” because of the suite of predictor variables
Composed of many Classification and Regression Tree (CART) models
Output: probability that a pixel belongs to a certain class
statistical models
Notes: Apply RF model for a given class on pixel-wise basis to generate model outputs
E.g. 4 out of 5 trees predicted grass (60% probability)
We use thresholding for the change product ( thresholding is based on accuracy assessment using predicted and validation data) to determine if change occurred or not.
If we take the class with the majority of the votes, this pixel would be grass

## Slide 47: LCMS Raw Products Probability
Notes: The raw products of the LCMS workflow are the probability that a pixel belongs to a given class.
Map assemblage, converts these outputs into the final outputs, with classes, that you saw at the beginning of this section.

## Slide 48: LCMS Raw Products Probability
For example:
Loss Probability
Proportion of Random Forest model votes for “Loss”
Ranges from 0.00-1.00
Gain Probability
Proportion of Random Forest model votes for “Gain”
Ranges from 0.00-1.00
Notes: The raw products of the LCMS workflow are the probability that a pixel belongs to a given class.
Map assemblage converts these outputs into the final outputs, with classes, that you saw at the beginning of this section.

## Slide 49: LCMS Workflow Map assemblage
Crop
Grass
Grass
Shrub
Grass
Class | Prob. | Final class
Grass | 60% | GRASS
Shrub | 20% | 
Crop | 20% | 
Highest probability assemblage:
  Class with the most votes from trees gets the pixel
We use this for land cover and land use
map assemblage
Notes: DUPE FOR ACCESSIBLE IMAGES
The raw products of the LCMS workflow are the probability that a pixel belongs to a given class.
Map assemblage converts these outputs into the final outputs, with classes, that you saw at the beginning of this section.

## Slide 50: LCMS Workflow Map assemblage
Highest probability assemblage:
  Class with the most votes from trees gets the pixel
We use this for land cover and land use
map assemblage
Class | Prob. | Final class
Grass | 60% | GRASS
Shrub | 20% | 
Crop | 20% | 
Notes: The raw products of the LCMS workflow are the probability that a pixel belongs to a given class.
Map assemblage converts these outputs into the final outputs, with classes, that you saw at the beginning of this section.

## Slide 51: LCMS Workflow Map assemblage
Model thresholding:
  Calculate a threshold for each class that balances omission and commission
Class with the highest probability that also exceeds its threshold gets the pixel
map assemblage
Change classes
Probability value
Class probability thresholds
Class assigned to the pixel
Notes: DUPE FOR ACCESSIBLE IMAGES
The raw products of the LCMS workflow are the probability that a pixel belongs to a given class.
Map assemblage, converts these outputs into the final outputs, with classes, that you saw at the beginning of this section.

## Slide 52: LCMS Workflow Map assemblage
Model thresholding:
  Calculate a threshold for each class that balances omission and commission
Class with the highest probability that also exceeds its threshold gets the pixel
map assemblage
Notes: The raw products of the LCMS workflow are the probability that a pixel belongs to a given class.
Map assemblage, converts these outputs into the final outputs, with classes, that you saw at the beginning of this section.

## Slide 53: 1.4: LCMS Applications

## Slide 54: Example applications
Land use / land cover change
Hydrologic modeling
Vegetation mapping
Deforestation monitoring
Hurricane response
Insect and disease monitoring
Post-fire and post-harvest recovery
Forest planning and revision
Notes: LCMS data products have been extensively used by the Forest Service, as well as by the USGS and NOAA.
Example at right: monitoring recession of Great Salt Lake, Utah, USA
Examples of applications include:
  The Flathead National Forest in Region 1 compared rates of recovery based on LCMS data after silvicultural treatments
  Manti - La Sal National Forest in Region 4 used LCMS data to determine extent of prior year’s beetle kill for field work planning
  Region 8 (Southeastern US) plans to use LCMS data in applications including hurricane response and insect and disease monitoring.
  Region 10 (Southeastern Alaska) uses LCMS for insect and disease monitoring

## Slide 55: Example applications
Land use / land cover change
Hydrologic modeling
Vegetation mapping
Deforestation monitoring
Hurricane response
Insect and disease monitoring
Post-fire and post-harvest recovery
Forest planning and revision
Florida Panhandle, Hurricane Michael, 2018
Notes: LCMS data products have been extensively used by the Forest Service, as well as by the USGS and NOAA.
Example at right: Impacts of Hurricane Michael - hurricane event was 2018. Apalachicola, Florida Panhandle, southeastern US
Examples of applications include:
compare rates of forest recovery after silvicultural treatments based on LCMS data - (The Flathead National Forest in Region 1)
Determine extent of prior year’s beetle kill for field work planning (Manti - La Sal National Forest in Region 4)
Hurricane response (planned by region 6)

## Slide 56: Case Study: Colorado Front Range
USFS Region 2
Multiple change agents and change types
Post-fire recovery

## Slide 57: Case Study: Colorado Front Range
USFS Region 2
Multiple change agents and change types
Post-fire recovery
Cameron Peak fire, 2020
Image: Cameron Peak Fire, 10/15/2020. Via Google Earth.

## Slide 58: Case Study: Colorado Front Range

## Slide 59: Case Study: Colorado Front Range
2011

## Slide 60: Case Study: Colorado Front Range
2012

## Slide 61: Case Study: Colorado Front Range
2013

## Slide 62: Case Study: Colorado Front Range
2019

## Slide 63: Case Study: Colorado Front Range
2021

## Slide 64: Case Study: Colorado Front Range

## Slide 65: Case Study: Colorado Front Range
2019

## Slide 66: Case Study: Colorado Front Range
2022

## Slide 67: Case Study: Colorado Front Range
2005

## Slide 68: Case Study: Colorado Front Range
2011

## Slide 69: Case Study: Colorado Front Range
2005

## Slide 70: Case Study: Colorado Front Range
2009

## Slide 71: Case Study: Colorado Front Range

## Slide 72: Questions?

## Slide 73: Break – 15 minutes

## Slide 74: 2.1: LCMS Data Explorer Demo

## Slide 75: Meet the LCMS Data Explorer.
Land use, land cover, and landscape change, dating back to 1985.
Notes: Advanced capabilities can display all of the layers discussed previously, and all the layers listed on the left.
Key capabilities are:
Ability to explore change, land use, and land cover for present day and time lapses
Inspect probability of loss and gain over time
Examine duration of slow loss events
Export query results for a point or an area to use in other applications
An example that you can use for inspiration when developing your own tools!
https://apps.fs.usda.gov/lcms-viewer/

## Slide 76: 2.2: LCMS Data in ArcPro

## Slide 77
Image server:
https://apps.fs.usda.gov/fsgisx01/rest/services/RDW_LandscapeAndWildlife

## Slide 78: 2.3: LCMS Data in the GEE Catalog

## Slide 79
https://developers.google.com/earth-engine/datasets/catalog/USFS_GTAC_LCMS_v2022-8

## Slide 80: Questions?
Lila Leatherman (they/them)
Remote Sensing Specialist and Trainer
Contractor, Redcastle Resources
Lila.Leatherman@usda.gov
LCMS Homepage